## Slide 1: POM
How to use ?

## Slide 2: POM and INSITU
POM module uses 2 libraries:
  PoM: Position Manager
  Centralizes all the estimated positions of the robot.
  InSitu: Internal Situation
  Manages the graph (the links) of the frames on the robot.

## Slide 3: Robot positions managment
All the Motion Estimators (ME) export their robot position for POM
POM produces one fused position for the robot (relative and absolute)

## Slide 4: Frames Positions
All the Sensors Estimators (SE) export their sensor position for POM
POM produces one position for each (sensor) frame on robot frame
All the data must be tagged at acquisition time with its sensor configuration exported by POM.

## Slide 5: InSitu: Rackham example

## Slide 6: Example: Rackham’s frames
# b21r geometric model -------
# Frame declarations
frame CameraTop;
frame CameraEVI;
frame Platine;
frame Sick;
frame Robot;
# The common frame
main Robot;
# Links descriptions
link {
from CameraTop;
to Platine;
translate 0.0 0.0 0.075;
rotate 0.0 0.0 0.0;
}
link {
from Platine;
to Robot;
translate 0.2 0.0 1.81;
rotate 0.0 0.0 0.0;
}
link {
from Sick;
to Robot;
translate -0.04 0.0 0.38;
rotate 0.0 0.0 0.0;
}
link {
from CameraEVI;
to Robot;
translate 0.065 -0.08 1.64;
rotate 1.526 0.0 1.526;
}

## Slide 7: InSitu: Jido example

## Slide 8: InSitu: Jido example
# Jidowanki geometric model -----------------
# Frame declarations
#--- base
# center of wheel axis projected onto floor
frame Robot;
# center of front SICK (motorized)
frame FrontSick;
# center of rear SICK
frame RearSick;
# camera on pole
frame PoleCamera;
#--- arm etc
# z y
# |/
# R6*-x
# |
# * y
# |/
# Base*-x
# |
# +----------+
# | |
# | | front
# +----------+
# mount point of robot arm
frame BaseArm;
# position of last link of the arm
frame R6Arm;
link {
from Robot;
to BaseArm;
translate 0.180 0.0 0.924;
rotate 0.0 0.0 0.0;
}
link {
from Robot;
to R6Arm;
translate 0.0 0.0 0.930;
rotate 0.0 0.0 0.0;
}
link {
from R6Arm;
to Force;
translate 0.0 0.0 0.100;
rotate 0.0 0.0 0.0;
}
link {
from Robot;
to Gripper;
translate 0.0 0.0 0.150;
rotate 0.0 0.0 0.0;
}
link {
from R6Arm;
to ArmCamera;
translate -0.100 0.0 0.125;
rotate 0.0 0.0 0.0;
}
# 6DOF force sensor (wrist)
frame Force;
# Gripper
frame Gripper;
# camera on arm
frame ArmCamera;
# main frame
main Robot;
# Link declarations
link {
from Robot;
to FrontSick;
translate 0.350 0.0 0.270;
rotate 0.0 0.0 0.0;
}
link {
from Robot;
to RearSick;
translate -0.350 0.0 0.270;
rotate 0.0 0.0 0.0;
}
link {
from Robot;
to PoleCamera;
translate 0.0 0.0 0.0;
rotate 0.0 0.0 0.0;
}

## Slide 9: InSitu within Pom module
PoM module exportes 1 poster per frame « pom<FramecdName>Pos »
Structure POM_SENSOR_POS:
    typedef struct POM_SENSOR_POS {
    int date; /* time of acquisition */
    int pad;
    POM_EULER_V sensorToMain; /* transformation from the sensor's frame to the
    * main robot's frame */
    POM_EULER_V mainToBase; /* transformation from the robot's main frame to
    * the current local frame */
    POM_EULER_V mainToOrigin; /* transformation from the robot's main frame to
    * the global absolute frame */
    POM_EULER_V VLocal; /* Local velocities */
    } POM_SENSOR_POS;

## Slide 10: Structure position POM_EULER_V
    typedef struct POM_EULER_V {
    POM_EULER euler;
    POM_EULER_VARIANCE var;
    } POM_EULER_V;
    typedef struct POM_EULER {
    double yaw, pitch, roll;
    double x, y, z;
    } POM_EULER;
    typedef struct POM_EULER_VARIANCE {
    double voo;
    double vop, vpp;
    double vor, vpr, vrr;
    double vox, vpx, vrx, vxx;
    double voy, vpy, vry, vxy, vyy;
    double voz, vpz, vrz, vxz, vyz, vzz;
    } POM_EULER_VARIANCE;

## Slide 11: Using: A Motion Estimator (ME) module
In .gen :
requires: pom;
Import from pom {
pomStruct.h
};
/* Motion Estimator Poster*/
poster MEPos {
update: user;
type: POM_ME_POS;
exec_task: PosterTask;
};

## Slide 12: Utilization: a Motion Estimator (ME) module
In codels:
  #include "pomStruct.h" /* pom ME client library */
Structure produced by a motion estimator:
  typedef struct POM_ME_POS {
  POM_ME_CLASS class; /* POM_ME_ABSOLUTE or POM_ME_DELTA */
  int unused;
  double confidence; /* must be in [0-1] */
  int date1;
  int date2; /* to disapear */
  POM_EULER_V main; /* mainToOrigin */
  POM_EULER_V VLocal;
  } PomMEPos;

## Slide 13: Utilization: a Sensor Estimator (SE) module
In codels:
  #include "pomStruct.h" /* pom ME client library */
Structure produced by a Sensor Estimator (SE):
  typedef struct POM_SENSOR_POS {
  int date;
  int pad;
  POM_EULER_V sensorToMain;
  POM_EULER_V mainToBase;
  POM_EULER_V mainToOrigin;
  POM_EULER_V VLocal;
  } POM_SENSOR_POS;

## Slide 14: Utilization: a position consumer module
In .gen:
        /* posters updating */
        exec_task PosterTask {
        period: RFLEX_TICKS_PERIOD;
        delay: 3;
        priority: 30;
        stack_size: 800000;
        c_init_func: rflexPosterTaskInit;
        c_end_func: rflexPosterTaskEnd;
        c_func: rflexPosterTrackPerm;
        posters_input: POM_SENSOR_POS;
        };

## Slide 15: Utilization: a position consumer module
In codels:
    /* Get the pom's current position */
    if (SDI_F->pomTagging == RFLEX_ENABLE_POMTAGS) {
    if (posterFind("pomRobotFramePos",&pomFrameId) != OK) {
    fputs("rflex: could not get frame\n", stderr);
    pomFrameId = NULL;
    *bilan = S_rflexPumpTask_POSTER_NOT_FOUND;
    return ETHER;
    }
    if (rflexPOM_SENSOR_POSPosterRead(pomFrameId,&firstFrame) != OK) {
    fputs("rflex: could not read frame\n", stderr);
    pomFrameId = NULL;
    *bilan = S_rflexPumpTask_POSTER_NOT_FOUND;
    return ETHER;
    }
    }

## Slide 16: Utilization: running Motion or Sensor Estimators
Script tcl :
  ## INSITU
  pom::SetModel /usr/local/openrobots/data/robots/rackham/geom/b21r.geom
  ## RFLEX / POM
  rflex::PomTagging RFLEX_ENABLE_POMTAGS
  pom::AddME rflex POM_FUSE 0
  pom::SetRefME rflex
  pom::Run POM_START
## PLATINE/POM
  platine::InitDriver /dev/ttyR7 9600
  pom::AddSE platine Platine Robot 0

## Slide 17: Doc/Examples
Docs: …/modules/pom/doc
Examples:
  Module rflex (mainly codels/rflexPostersTaskCodels.c)
  Module platine